## Slide 1: RISCME Microarchitecture (Reduced Instruction Set Cortex M Educational Microarchitecture)
Jardel Silveira
Jorge Reis
LESC/DETI/UFC

## Slide 2: Requirements for RISCME
Micro Architecture: Single Cycle (So it’s not cycle accurate to ARMV6-M)
Instruction Set: ARMV6-M Thumb 16 bits
  Supported instructions: B,BX,BLX,LDR,STR,ANDS,ORRS,ADDS,SUBS
  Not All encoding of theses instructions are supported, but only listed one in this presentation
Accessible registers : R0-R7 and R15 and LR
Language: System Verilog
Synthesizable ? YES !!
Stack pointer Instructions ? No !
Must be compatible with any assembler, like gcc or mdk, configured to generate cortex m0 binary
Datapath must be similar to Harris & Harris ARM7 Educational Single Cycle ARM

## Slide 3
Microarchitecture

## Slide 4
opcode | Instruction class
00xxxx | Adds and Subs
010000 | Data processing (ands / orrs)
010001 | Branch and Exchange
0101xx 011xxx 100xxx | Load/store single data item
1101xx | Conditional branch
11100x | Unconditional Branch
16-bit Thumb Instruction Enconding

## Slide 5
Op | Type | Branch | MemtoReg | MemW | ALUSrc | ImmSrc | RegW | RegSrc | LRW | FlagW | ALUControl
0001100 0001101 | DPRSP | 0 | 0 | 0 | 0 | XX | 1 | 0XX10 | 0 | 11 | 0?
0100000000 0100001100 | DPRCM | 0 | 0 | 0 | 0 | XX | 1 | 0XX00 | 0 | 10 | 1?
00110 00111 | DP Imm | 0 | 0 | 0 | 1 | 01 | 1 | 10XX1 | 0 | 11 | 0?
01100 | STR | 0 | X | 1 | 1 | 00 | 0 | 0XX0X | 0 | 00 | 00
01101 | LDR | 0 | 1 | 0 | 1 | 00 | 1 | 0XXX0 | 0 | 00 | 00
11100 | B | 1 | 0 | 0 | 1 | 11 | 0 | 110XX | 0 | 00 | 00
1101 | B cond | 1 | 0 | 0 | 1 | 10 | 0 | 110XX | 0 | 00 | 00
010001110 | BX | 1 | 0 | 0 | 0 | XX | 0 | 1110X | 0 | 00 | 00
010001111 | BLX | 1 | 0 | 0 | 0 | XX | 0 | 1110X | 1 | 00 | 00

## Slide 6
opcode | Instruction class
00xxxx | Add and Sub
Adds and Subs

## Slide 7
ADDS e SUBS
opcode | Instruction
01100 | Adds Register
01101 | Subs Register
110xx | Adds 8-bit imm
111xx | Subs 8-bit imm

## Slide 8: ADDS (Immediate)

## Slide 9: ADDS (Register)

## Slide 10: SUBS (Immediate)

## Slide 11: SUBS (Register)

## Slide 12
opcode | Instruction class
010000 | Data processing
Data Processing Instructions

## Slide 13
ORRS e ANDS
opcode | Instruction
0000 | Bitwise And
1100 | Logical or

## Slide 14: ANDS (Register)

## Slide 15: ORRS (Register)

## Slide 16
opcode | Instruction class
010001 | Branch and Exchange
Branch and Exchange

## Slide 17
BLX and BX
opcode | Instruction
110x | BX
111x | BLX

## Slide 18: BLX (Register)

## Slide 19: BX (Register)

## Slide 20
opcode | Instruction class
0101xx 011xxx 100xxx | Load/store single data item
Load/store single data item

## Slide 21
LDR e STR
opA | opB | Instruction
0110 | 0xx | STR Imm
0110 | 1xx | LDR Imm

## Slide 22: LDR (Immediate)

## Slide 23: STR (Immediate)

## Slide 24
opcode | Instruction class
1101xx | Conditional branch
Conditional branch

## Slide 25
B

## Slide 26: B

## Slide 27
opcode | Instruction class
11100x | Unconditional Branch
Unconditional Branch

## Slide 28: B

## Slide 29
 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DP Reg |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADDS <Rd>,<Rn>,<Rm> | 0 | 0 | 0 | 1 | 1 | 0 | 0 | Rm |  |  | Rn |  |  | Rd |  | 
SUBS <Rd>,<Rn>,<Rm> | 0 | 0 | 0 | 1 | 1 | 0 | 1 | Rm |  |  | Rn |  |  | Rd |  | 
ANDS <Rdn>,<Rm> | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Rm |  |  | Rdn |  | 
ORRS <Rdn>,<Rm> | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | Rm |  |  | Rdn |  | 
DP Imm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADDS <Rdn>,#<imm8> | 0 | 0 | 1 | 1 | 0 | Rdn |  |  | Imm8 |  |  |  |  |  |  | 
SUBS <Rdn>,#<imm8> | 0 | 0 | 1 | 1 | 1 | Rdn |  |  | Imm8 |  |  |  |  |  |  | 
LDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LDR <Rt>, [<Rn>{,<imm5>}] | 0 | 1 | 1 | 0 | 1 | imm5 |  |  |  |  | Rn |  |  | Rt |  | 
STR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
STR <Rt>, [<Rn>{,<imm5>}] | 0 | 1 | 1 | 0 | 0 | imm5 |  |  |  |  | Rn |  |  | Rt |  | 
Branch |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
B<c> <label> | 1 | 1 | 0 | 1 | cond |  |  |  | Imm8 |  |  |  |  |  |  | 
B <label> | 1 | 1 | 1 | 0 | 0 | Imm11 |  |  |  |  |  |  |  |  |  | 
BLX <Rm> | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | Rm |  |  |  | 0) | 0) | 0)
BX <Rm> | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | Rm |  |  |  | 0) | 0) | 0)

## Slide 30: References
ARMv6-M Architecture Reference Manual
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi0419c/index.html
  https://imagecraft.com/pub/ARM/DDI0419C.pdf
http://pages.hmc.edu/harris/class/e85/arm_single.sv
http://pages.hmc.edu/harris/class/e85/DDCAarm_Ch7.pptx